## Slide 1: Evaluation of Direct Level-Set Ray Tracing Performance on GPUs for Process Simulation Applications 360.245 Selected Topics - Computational Electronics Mario Hiti

## Slide 2: Signed distance function Φ
Φ(x) returns the shortest distance between x and the surface ∂Ω
Sign determines if point is on the inside or outside
Very easy to simulate surface advection
Notes: Shortest distance
Sign
Advection
Don’t store formula but values of phi in a volumetric grid

## Slide 3: Narrow Band Level-Sets
Store values of Φ(x) in a discrete grid
Φ(|x| >> 0) irrelevant
  only store values near the surface boundary
  all other voxels are inactive
Very well suited for raytracing

## Slide 4: Raytracing
Ray origin
Intersection:
The sign of Φ(x) changes
Narrow band
active Voxels
Inactive Voxels
Notes: Start somewhere and step to next voxel
Fast in coarse grid
Then slow
Interseciton
Sign change

## Slide 5: Applications
Notes: Multiple sources
Reflections, absorptions
Boundary conditions

## Slide 6: Frameworks
OpenVDB
Released in 2012
Mature and rich in features
CPU only
Allows changes to the narrow band
Complex build process
Several dependencies
NanoVDB
Released in 2021
Many features missing or incomplete
CPU and/or GPU (CUDA)
Recompute everything when narrow band changes
Header only
No dependencies

## Slide 7: Goal
NVIDIA released a benchmark promising a 60x increase in performance
Can we expect the same performance for our simulations?
https://developer.nvidia.com/blog/accelerating-openvdb-on-gpus-with-nanovdb
60x faster!
Notes: NVIDAI promises 60x increase in perf
Question: can we expect the same
Details are vague at best, and they usually try to sell a best-case scenario
We aimed to design a worst-case benchmark

## Slide 8: The worst-case Scenario
Typical Application
Modified Setup
Pre-comupte n rays
Calculate intersections
Verify results
Increase n and goto 1.
Workflow
Notes: Rays being cast down a trench
already quite difficult
2 spheres within each other
Rays exit inner narrow band, traverse ccoarse grid, reenter narrow band
All rays intersect
Offset
Some other measures: Rays are shuffled

## Slide 9: Hardware
Benchmark performed on a TCAD Cluster provided by IuE
Hardware | Price | Power Consumption | Cores
Intel Xeon 6248 | 3.300 € | 105W | 20 Cores, 40 Threads
NVIDIA Tesla T4 | 3.000 € | 70W | 2.560 CUDA-Cores
Notes: CPU and GPU are different
Comparing apples to oranges
Similar price and power consumption

## Slide 10: Benchmark Results
Rays per Second (parameter-sweep)
Rays per second for n ≈ 5mio
6.2x faster
Notes: X axis
Y axis
Small size
Big size
6.2x faster

## Slide 11: NanoVdb: The Good
Performance is great
Very good code quality, no bugs encountered
Target platform is determined at compile time
  Same code for CPU and GPU
  Develop on PC (no GPU necessary), deploy on cluster
  Calculation can run on CPU and GPU in parallel → add performance of both

## Slide 12: Nanovdb: The bad
No boundary conditions (periodic or reflective)
  Can be implemented
Raytracing is inaccurate (see image)
  Can be improved
Realistically OpenVDB is still needed → difficult to compile on cluster
  Can be automated
Raytracing accuracy

## Slide 13: Nanovdb: The ugly
Difficult to learn
poor documentation (especially for NanoVDB)
Limited compatibility between OpenVDB and NanoVDB
Lots of template meta-programming and boiler-plate code

## Slide 14: Outlook and further topics
Expand NanoVDB for process simulations
  Implement reflections
  Implement boundary conditions
  Increase accuracy of raytracing
  Moving ray sources
  …
Further improve performance
  branchless programming
  Use more GPU features such as CUDA streams
  Multiple GPUs
  Combine CPU + (multiple) GPU
  RTX?
  …

## Slide 15: Questions

## Slide 16: Appendix: Simulation setup
3D spheres
Rays are shuffled in memory
No reflections
Volumetric ray source
Offset sphere for distribution of ray lengths
No ray leaves bounding box
All rays leave narrow band, traverse inactive cells and reenter narrow band
Time for ray generation not included
Rays are reused if (V)RAM is full
All calculations are verified
No repetitions
Only single precision
Notes: Rays are shuffled
no reflections
all rays intersect
leave narrow band
Leave narrow band
traverse inactive voxels and reenter the narrow band

## Slide 17: Appendix: accuracy
NanoVDB stops when a voxel containing the intersection point is found
Realistically only useful to determine IF the ray intersects
OpenVDB uses neighboring voxels to approximate real intersection point
Most likely (part of) the reason why NanoVDB is faster on CPU

## Slide 18: Appendix: BRANCHLESS programming
GPUs use SIMT architecture (single instruction multiple thread)
Threads are grouped in “warps” (usually 32 threads = 1 warp)
Problem: branches
Threads execute both branches sequentially and a mask determines which branch has an effect
Branchless programming:
x = (a > b) ? C : D; // branches
x = (a > b) * C + (a <= b) * D; // no branches